## Slide 1: MICROPROGRAMMED CONTROL
  Control Memory
  Sequencing Microinstructions
  Microprogram Example
  Design of Control Unit
  Microinstruction Format
  Nanostorage and Nanoprogram

## Slide 2: COMPARISON OF CONTROL UNIT IMPLEMENTATIONS
Implementation of Control Unit
Control Unit Implementation
Combinational Logic Circuits (Hard-wired)‏
Microprogram
I R
Status F/Fs
Control Data
Combinational
Logic Circuits
Control
Points
CPU
Memory
Timing State
Ins. Cycle State
Control Unit's State
Status F/Fs
Control Data
Next Address
Generation
Logic
C
S
A
R
Control
Storage
(-program
memory)‏
M
e
m
o
r
y
I R
C
S
D
R
C
P
s
CPU
D
}

## Slide 3: TERMINOLOGY
Microprogram
- Program stored in memory that generates all the control signals required
to execute the instruction set correctly
- Consists of microinstructions
Microinstruction
- Contains a control word and a sequencing word
Control Word - All the control information required for one clock cycle
Sequencing Word - Information needed to decide
the next microinstruction address
- Vocabulary to write a microprogram
Control Memory(Control Storage: CS)‏
- Storage in the microprogrammed control unit to store the microprogram
Writeable Control Memory(Writeable Control Storage:WCS)‏
- CS whose contents can be modified
-> Allows the microprogram can be changed
-> Instruction set can be changed or modified
Dynamic Microprogramming
- Computer system whose control unit is implemented with
a microprogram in WCS
- Microprogram can be changed by a systems programmer or a user

## Slide 4: TERMINOLOGY
Sequencer (Microprogram Sequencer)‏
A Microprogram Control Unit that determines
the Microinstruction Address to be executed
in the next clock cycle
- In-line Sequencing
- Branch
- Conditional Branch
- Subroutine
- Loop
- Instruction OP-code mapping

## Slide 5: MICROINSTRUCTION SEQUENCING
Sequencing Capabilities Required in a Control Storage
- Incrementing of the control address register
- Unconditional and conditional branches
- A mapping process from the bits of the machine
instruction to an address for control memory
- A facility for subroutine call and return
Sequencing
Instruction code
Mapping
logic
Multiplexers
Control memory (ROM)‏
Subroutine
register
(SBR)‏
Branch
logic
Status
bits
Microoperations
Control address register
(CAR)‏
Incrementer
MUX
select
select a status
bit
Branch address

## Slide 6: CONDITIONAL BRANCH
Unconditional Branch
Fixing the value of one status bit at the input of the multiplexer to 1
Sequencing
Conditional Branch
If Condition is true, then Branch (address from
the next address field of the current microinstruction)‏
else Fall Through
Conditions to Test: O(overflow), N(negative),
Z(zero), C(carry), etc.
Control address register
Control memory
MUX
Load address
Increment
Status
(condition)‏
bits
Micro-operations
Condition select
Next address
...

## Slide 7: MAPPING OF INSTRUCTIONS TO MICROROUTINES
Mapping function implemented by ROM or PLA
OP-code
Mapping memory
(ROM or PLA)‏
Control address register
Control Memory
Mapping from the OP-code of an instruction to the
address of the Microinstruction which is the starting
microinstruction of its execution microprogram
1 0 1 1 Address
OP-code
Mapping bits
Microinstruction
address
0 x x x x 0 0
0 1 0 1 1 0 0
Machine
Instruction
Sequencing

## Slide 8: MICROPROGRAM EXAMPLE
Microprogram
Computer Configuration

## Slide 9: MACHINE INSTRUCTION FORMAT
Microinstruction Format
Microprogram
EA is the effective address
Symbol OP-code Description
  ADD 0000 AC AC + M[EA]
  BRANCH 0001 if (AC < 0) then (PC  EA)‏
  STORE 0010 M[EA]  AC
  EXCHANGE 0011 AC M[EA], M[EA]  AC
Machine instruction format
I
Opcode
15
14
11
10
Address
0
Sample machine instructions
F1
F2
F3
CD
BR
AD
3
3
3
2
2
7
F1, F2, F3: Microoperation fields
CD: Condition for branching
BR: Branch field
AD: Address field

## Slide 11: SYMBOLIC MICROINSTRUCTIONS
Symbols are used in microinstructions as in assembly language
A symbolic microprogram can be translated into its binary equivalent by a microprogram assembler.
Sample Format
five fields: label; micro-ops; CD; BR; AD
  Label: may be empty or may specify a symbolic address terminated with a colon
  Micro-ops: consists of one, two, or three symbols
  separated by commas
  CD: one of {U, I, S, Z}, where U: Unconditional Branch
  I: Indirect address bit
  S: Sign of AC
  Z: Zero value in AC
  BR: one of {JMP, CALL, RET, MAP}
  AD: one of {Symbolic address, NEXT, empty}
Microprogram

## Slide 12: SYMBOLIC MICROPROGRAM - FETCH ROUTINE
AR PC
DR  M[AR], PC  PC + 1
AR  DR(0-10), CAR(2-5)  DR(11-14), CAR(0,1,6)  0
Symbolic microprogram for the fetch cycle:
ORG 64
PCTAR U JMP NEXT
READ, INCPC U JMP NEXT
DRTAR U MAP
FETCH:
Binary equivalents translated by an assembler
1000000 110 000 000 00 00 1000001
1000001 000 100 101 00 00 1000010
1000010 101 000 000 00 11 0000000
Binary
address F1 F2 F3 CD BR AD
Microprogram
During FETCH, Read an instruction from memory
and decode the instruction and update PC
Sequence of microoperations in the fetch cycle:

## Slide 13: SYMBOLIC MICROPROGRAM
Control Storage: 128 20-bit words
The first 64 words: Routines for the 16 machine instructions
The last 64 words: Used for other purpose (e.g., fetch routine and other subroutines)‏
Mapping: OP-code XXXX into 0XXXX00, the first address for the 16 routines are
0(0 0000 00), 4(0 0001 00), 8, 12, 16, 20, ..., 60
Microprogram
ORG 0
NOP
READ
ADD
ORG 4
NOP
NOP
NOP
ARTPC
ORG 8
NOP
ACTDR
WRITE
ORG 12
NOP
READ
ACTDR, DRTAC
WRITE
ORG 64
PCTAR
READ, INCPC
DRTAR
READ
DRTAR
I
U
U
S
U
I
U
I
U
U
I
U
U
U
U
U
U
U
U
CALL
JMP
JMP
JMP
JMP
CALL
JMP
CALL
JMP
JMP
CALL
JMP
JMP
JMP
JMP
JMP
MAP
JMP
RET
INDRCT
NEXT
FETCH
OVER
FETCH
INDRCT
FETCH
INDRCT
NEXT
FETCH
INDRCT
NEXT
NEXT
FETCH
NEXT
NEXT
NEXT
ADD:
BRANCH:
OVER:
STORE:
EXCHANGE:
FETCH:
INDRCT:
Label Microops CD BR AD
Partial Symbolic Microprogram

## Slide 14: BINARY MICROPROGRAM
This microprogram can be implemented using ROM
Microprogram
  Address Binary Microinstruction
  Micro Routine Decimal Binary F1 F2 F3 CD BR AD
ADD 0 0000000 000 000 000 01 01 1000011
  1 0000001 000 100 000 00 00 0000010
  2 0000010 001 000 000 00 00 1000000
  3 0000011 000 000 000 00 00 1000000
BRANCH 4 0000100 000 000 000 10 00 0000110
  5 0000101 000 000 000 00 00 1000000
  6 0000110 000 000 000 01 01 1000011
  7 0000111 000 000 110 00 00 1000000
STORE 8 0001000 000 000 000 01 01 1000011
  9 0001001 000 101 000 00 00 0001010
  10 0001010 111 000 000 00 00 1000000
  11 0001011 000 000 000 00 00 1000000
EXCHANGE 12 0001100 000 000 000 01 01 1000011
  13 0001101 001 000 000 00 00 0001110
  14 0001110 100 101 000 00 00 0001111
  15 0001111 111 000 000 00 00 1000000
FETCH 64 1000000 110 000 000 00 00 1000001
  65 1000001 000 100 101 00 00 1000010
  66 1000010 101 000 000 00 11 0000000
INDRCT 67 1000011 000 100 000 00 00 1000100
  68 1000100 101 000 000 00 10 0000000

## Slide 15
Design of Control Unit
Fig. Decoding of micro-operations fields

## Slide 16: MICROPROGRAM SEQUENCER - NEXT MICROINSTRUCTION ADDRESS LOGIC -
Design of Control Unit
MUX-1 selects an address from one of four sources and routes it into a CAR
- In-Line Sequencing  CAR + 1
- Branch, Subroutine Call  CS(AD)‏
- Return from Subroutine  Output of SBR
- New Machine instruction  MAP

## Slide 17: MICROPROGRAM SEQUENCER - CONDITION AND BRANCH CONTROL -
Design of Control Unit
Input
logic
I0
I1
T
MUX2
Select
1
I
S
Z
Test
CD Field of CS
From
CPU
BR field
of CS
L(load SBR with PC) for subroutine Call
S0
S1
for next address
selection
I0I1T Meaning Source of Address S1S0 L
000 In-Line CAR+1 00 0
001 JMP CS(AD) 10 0
010 In-Line CAR+1 00 0
011 CALL CS(AD) and SBR <- CAR+1 10 1
10x RET SBR 01 0
11x MAP DR(11-14) 11 0
L
S0 = I0
S1 = I0I1 + I0’T
L = I0’I1T
Input Logic

## Slide 18: MICROINSTRUCTION FORMAT
Microinstruction Format
Information in a Microinstruction
- Control Information
- Sequencing Information
- Constant
Information which is useful when feeding into the system
These information needs to be organized in some way for
- Efficient use of the microinstruction bits
- Fast decoding
Field Encoding
- Encoding the microinstruction bits
- Encoding slows down the execution speed
due to the decoding delay
- Encoding also reduces the flexibility due to
the decoding hardware

## Slide 19: HORIZONTAL AND VERTICAL MICROINSTRUCTION FORMAT
Horizontal Microinstructions
Each bit directly controls each micro-operation or each control point
Horizontal implies a long microinstruction word
Advantages: Can control a variety of components operating in parallel.
--> Advantage of efficient hardware utilization
Disadvantages: Control word bits are not fully utilized
--> CS becomes large --> Costly
Vertical Microinstructions
A microinstruction format that is not horizontal
Vertical implies a short microinstruction word
Encoded Microinstruction fields
--> Needs decoding circuits for one or two levels of decoding
Microinstruction Format
One-level decoding
Field A
2 bits
2 x 4
Decoder
3 x 8
Decoder
Field B
3 bits
1 of 4
1 of 8
Two-level decoding
Field A
2 bits
2 x 4
Decoder
6 x 64
Decoder
Field B
6 bits
Decoder and
selection logic

## Slide 20
Fig: Horizontal and Vertical microinstruction

## Slide 21
To execute this microinstruction, turn on all the control line indicated by a 1bit; leave off all control lines indicating by a 0 bit. The resulting control signals will cause one or more micro operations to be performed.
If the condition indicated by the condition bits is false, execute the next microinstruction in sequence.
If the condition indicated by the condition bits is true, the next microinstruction to be executed is indicated in the address field.
Horizontal microinstruction

## Slide 22: NANOSTORAGE AND NANOINSTRUCTION
The decoder circuits in a vertical microprogram
storage organization can be replaced by a ROM
=> Two levels of control storage
First level - Control Storage
Second level - Nano Storage
Two-level microprogram
First level
-Vertical format Microprogram
Second level
-Horizontal format Nanoprogram
- Interprets the microinstruction fields, thus converts a vertical microinstruction format into a horizontal nanoinstruction format.
Usually, the microprogram consists of a large number of short microinstructions, while the nanoprogram contains fewer words with longer nanoinstructions.
Control Storage Hierarchy

## Slide 23: TWO-LEVEL MICROPROGRAMMING - EXAMPLE
* Microprogram: 2048 microinstructions of 200 bits each
* With 1-Level Control Storage: 2048 x 200 = 409,600 bits
* Assumption:
256 distinct microinstructions among 2048
* With 2-Level Control Storage:
Nano Storage: 256 x 200 bits to store 256 distinct nanoinstructions
Control storage: 2048 x 8 bits
To address 256 nano storage locations 8 bits are needed
* Total 1-Level control storage: 409,600 bits
Total 2-Level control storage: 67,584 bits (256 x 200 + 2048 x 8)‏
Control Storage Hierarchy
Control address register
11 bits
Control memory
2048 x 8
Microinstruction (8 bits)‏
Nanomemory address
Nanomemory
256 x 200
Nanoinstructions (200 bits)‏